## Slide 1: Intro to Eagle

## Slide 2: Libraries and Parts
Symbol (pins & labels)
Footprint (dimensions & layout)
Device

## Slide 3: Schematics – Symbolic Diagrams
This is where you define components and values
Color codes
  Red = components
  Green = nets + buses (define physical connections)
Note - nets don’t need to be continuous. Label and split to improve readability.

## Slide 4: Routing – Designing the Actual Board
This is what the actual PCB will look like
Color codes:
  Green = pads (points where component is mounted on board)
  Red/Blue = routes (one on each side of the board)
    Note that thickness may vary
  Yellow = vias (switch sides)
    Try to minimize these
IMPORTANT: routes CANNOT cross

## Slide 5: Example Part: 555 Timer